## Slide 2: UART Protocol
Jordan Christman

## Slide 3: UART Protocol
Both the transmitting and receiving device must be aware of the following:
  Baud rate
  Number of Data bits
  Parity
  Number of Stop Bits

## Slide 4: UART Protocol
In binary we just transmitted:
  11010001b
This is known as little endian because we transmitted the LSB first
This example is sending 1 start bit, 8 data bits, no parity bits, and 1 stop bit.
1
0
0
0
1
0
Start bit
Stop bit
1
1
Next Start bit
LSB
MSB
Time 
Tx

## Slide 5: UART Protocol Timing
Assume 9600 baud
  1/9600 = 104.16 uS per bit
  So to send the 8 bits of data takes
    104.16 uS x 10 bits = 1,041.6 uS
1
0
0
0
1
0
Start bit
Stop bit
1
1
Next Start bit
LSB
MSB
104.16uS
1,041.6 uS