## Slide 2: UART Transmission Example
How do you actually transmit ASCII characters via UART?

## Slide 3: Transmission Example
I want to transmit “OK” from the FPGA to my computer.
Step 1) Look up ASCII values for letters O and K using an ASCII look up table and derive the associated binary representation. Look at the screen:
O(ASCII) = 4F(hex) = 01001111(binary)
K(ASCII) = 4B(hex) = 01001011(binary)
Step 2) Form the data packet by inserting the binary values for O and K as well as the start and stop bits.
Lets look at the UART data packet to send the letters OK

## Slide 4: Transmission Example
Here you can see the data packet we would send.
If your FPGA board were to send this packet of data to a serial port on your computer using TeraTerm as an example, you would see the letters OK, whereas your computer see’s the data shown in the data packet.
Note that the LSB is sent first because we are assuming that our serial port uses little endian.
Letter “O”
Letter “K”

## Slide 5: Transmission Example
Lets assume we are communicating at a baud rate of 115200. How long would we set the Tx line high and low?
1/115200 = 8.68uS
10 bits per character x 2 characters gives us 20 bits of data to transmit
20 bits x 8.68uS per bit = 173.6 uS