## Slide 2: Transmitter State Machine Design
We need to design a state machine that will control when data bits are shifted out on the Tx line

## Slide 3: Transmitter State Machine Diagram
shift
init
load
done_shifting = ‘1’
start_trans = ‘1’

## Slide 4: State Machine Design (Init State)
Init State
Set the transmit_done signal high
Check if the start_trans signal = ‘1’
  If yes  set next state to load
  Otherwise set next state to init
Check if the delay_clock_done signal = ‘1’
  If yes  set delay_clock signal to ‘0’
  Otherwise set delay_clock signal to ‘1’

## Slide 5: State Machine Design (Load / Shift State)
Load state
sets the load_data signal high
Shift state
checks if done_shifting = ‘1’
  If yes  set nxt_state signal to init and set the delay_clock to ‘1’
  Otherwise nxt_state stays at shift

## Slide 6: Transmitter State Machine Design
Now that you have completed the Transmitter design lectures get ready to implement this design on the FPGA!
END